## Slide 2
Action item
1.1 RTL to GDSII flow
1.2 PPA
1.3 Input file PnR : .gdc & .upf
1.4 DEF : input and output each stages
1.5 liberty contain
1.6 Different between LEF and DEF

## Slide 3
Architecture Specification
RTL Coding & Integration
RTL Verification
DFT, Synthesis
Physical Implementation
Post-layout Verification
Physical Verification and Sign-off
Tape-out
RTL Design
RTL Verification
Fabrication
Mask Tooling
Package & Test
Backend Integration (AC)
Physical Design (PI)
Production Services
Design Services

## Slide 4
Floorplan
Init design
Place Opt
Clock Concurrent optimization Technology (CCOPT)
Post -CTS
Routing
Post Route
PnR flow

## Slide 5
Init design
Define die/core area, utilization, I/O and macro locations, blockages, and pin placement
Target

## Slide 6
Floorplan
Define die/core area, utilization, I/O and macro locations, blockages, and pin placement
Target
Key outputs
Floorplan DEF with macros, IOs, rows, and blockages
Input:
Netlist (from Synthesis)
Technology LEF files
Design Constraints (SDC)
Macro LEF / Lib files
PDK & Design Rules

## Slide 7
Place Opt
Target Timing, power & area optimization Routable design Low cell & pin density Minimal congestion
Key output
Placed DEF, congestion and timing reports
Inputs Netlist Floorplan DEF Logical & physical libraries Design constraints Technology file

## Slide 8
Clock Concurrent optimization Technology (CCOPT)

## Slide 9
Post -CTS
Recover timing after clock-tree insertion changes delays
Optimized post-CTS netlist and timing reports
Target
Key outputs

## Slide 10
Routing
Key outputs
Target
Physically connect all signal nets using available metal layers without shorts or opens
Global and detailed routed DEF
Inputs:
CTS DEF, LEF, Technology/RC data, LIB

## Slide 11
Post Route
Key outputs
Target
Close timing using real parasitics; fix hold, setup, crosstalk, and DRC issues
Optimized routed design and timing reports

## Slide 12
Init design
LEF
Netlist (.v)
Liberty (.lib)
SDC
Other files

## Slide 13
Performance
Power
Area
Performance  timing
Power  congestion: when the number of routing tracks available for routing in a given location is less than the number necessary . The area is considered congested
Area  density

## Slide 14
Unified Power Format
(.upf)
Supply set definition
Power domain
Power switch
Retention cell
Level shifter cell
and other low power

## Slide 15
Netlist
It contains Logical connectivity Of all Cells
It contains List of nets Connecting
Each cell has its own instance/cell name and library/ref name

## Slide 16
Tech LEF or Header LEF
It contains physical information of standard cells, macros, pad
Contain the name of the pin, pin location (Co-ordinates) , pin layers, direction of pin (in,out, inout), uses of pin (Signal, Power, Ground) , height and width of the pin and cell.
Size of the cell (Height and width)
Symmetry of cell.
PHYSICAL LIBRARY

## Slide 17
Technology file
Contain manufacturing grid and site/unit tiles
Contain name, number convention of layer and via
Physical, electrical of layer and via
Physical design rule

## Slide 18
HEADER LEF
MACRO LEF

## Slide 19
LOGIC LIBRARIES
Physical Libraries
Timing / power / functionality
Timing : setup /hold / input delay
Power : internal power and leadkage power
Cell functionality : and / or/ not / xor
PVT condition
Technology LEF and Marco LEF
Tech LEF : physical info of metal layer and vias
IO cell : physical info of all input and output cells
DEF
Exact location information / height / width / rows / tracks

## Slide 20
Add Fillers
Physical Verification
Timing met
Design Import
Create and load Floorplan
Timing Mode
Scan Definition
Cell placement + Pre CTS opt
CTS + Post CTS setup Fixing
Post CTS Hold Fixing
Routing
Post Route opt
Timing met
Timing met
Timing met
Flase
True
Flase
Flase
True
True

## Slide 21
RTL Design
Synthesis
Physical design
STA & Signoff
Post- silicon Validation
Gate level optimization
Floorplanning , placement , CTS, Routing optimization
Timing closure , slack analysic
Voltage scaling
Fsm optimization, Efficient coding

## Slide 22
Liberty(.lib)
Cell Characterization Data
Functional Descriptions
Operating Conditions
+ Timing data (propagation delay, setup/hold, transition times)
+ Power data (internal power, leakage)
voltage, temperature, process corner

## Slide 25
analysis_view
delay corner
Constraint mode
RC Corner
Cell delay
Net delay
SDC
Library set
Timing (.lib)
=
+
Functional, Scan, Sleep, Test…) ↔file SDC tương ứng.
affect
+
Source :File .lib (Liberty)
Cap table / QRC Tech file

## Slide 26
Cell delay
the factors that determine Cell Delay :
Input transition time
Output load (capacitance)
PVT condition in which the library is characterized (SS, FF, TT, voltage, temperature…)
RC Corner → Net Delay
Net Delay (interconnect delay) is calculated from the parasitic R and C of the wire.
RC Corner specifies the parasitic parameter set:
  Cmax / Cmin
  RCmax / Rcmin
  Typical
  Temperature (affects the resistivity of the metal)
RC Corner

## Slide 27
Floorplan
Init design
Placement
Post -CTS
Routing
Post Route
Updated DEF
Netlist + LEF+ DEF+SDC
DEF

## Slide 28
Floorplan
Init design
Place Opt
Clock Concurrent optimization Technology (CCOPT)
Post -CTS
Routing
Post Route
Marcos,pin location, Core boundary and area
New clock buffers/inverters/ICGs, clock nets split into sub-nets, cells resized/moved.
Std cells placed, plus new buffers/cells from pre-CTS optimization (resizing, buffering).
Hold buffers, sizing/moves from optDesign -postCTS.